## Slide 1: Design Review – 2.4-GHz Downconversion Mixer
Dylan Rosser
  Dept. of Electrical and Computer Engineering
  Carnegie Mellon University

## Slide 2: System
What systems run at 2.4GHz? (hint: everything)
  Wifi (IEEE 802.11b/g/n)
  Bluetooth
  Wireless phones
  ZigBee (IEEE 802.15.4)
  Wireless Microphones
  Baby monitors
  Garage Opener
Blame your microwave
  https://www.wired.com/2010/09/wireless-explainer/
ISM Band (2.4GHz is one of several)
  Industrial, Scientific, Medical
  Unregulated (unlicensed)
Source: https://www.wired.com/2010/09/wireless-explainer/
Notes: Systems or applications for this design.
Microwaves are the reason so many devices are centered around 2.4GHz (2.45GHz is the standard for microwaves)

## Slide 3: Motivation
Channel selection filtering proves difficult at high frequencies
A mixer is capable of translating the desired channel to a lower center frequency
Impulses at shift desired channel to
  After filtering, signal is at a center frequency of
Heterodyne vs. direct conversion

## Slide 4: Motivations
RF Microelectronics, Razavi, Ch. 6
H. Darabi, A. A. Abidi, “Noise in RF CMOS mixers: a simple physical model,” IEEE J. of Solid-State Circuits, vol. 35, pp. 15-25, Jan. 2000.

## Slide 5: Specifications

## Slide 6: Proposed Topology
Double Balanced topology for differential RF input
Rejection of LO noise at the cost of input referred noise and power

## Slide 7: Analysis – Conversion Gain
M2 & M3 should not enter the triode so long as both carry current
]
  The max drop across the load resistors must accommodate the overdrive of M1 and 1.7x the equilibrium overdrive of each switching transistor
  For a given power budget, you can calculate the maximum RD
The equilibrium overdrive of the switching transistors can be reduced by making them wider.
Gain is reduced when both switching transistors are on (∆T)

## Slide 8: Analysis - Noise
Overdrive voltages and DC drop on load may be inflexible
  Sacrifice Power for noise performance
  Minimize ∆T
  LO transition time can also contribute to noise
Flicker noise substantial for IF near 0 & narrow bandwidth
1/f noise is scaled by IssRD/πVp,LO as it appears at the output
  Reduce bias current of switching devices to reduce 1/f noise
  Trade-off between thermal noise & flicker noise with current?
  Increase VpLO, area

## Slide 9: Analysis - Linearity
The input transistor imposes a direct trade-off between linearity and noise
The headroom consumed by the input transistor (Vgs – Vth) lowers the conversion gain
High gain can introduce compression at the output (switching devices introducing nonlinearity)

## Slide 10: Analysis - Excel
Mixer Design |  |  |  |  |  | 
Assuming a Power Budget for the mixer of |  |  |  |  | 8.00E-03 | W
At a VDD of |  |  |  |  | 1.2 | V
The tail current should be |  |  |  |  | 6.67E-03 | A
Design M1 |  |  |  |  |  | 
M1 | Vth | Vov | gm |  | Id | Think about M1 Vov
 | 0.4 | 0.3 | 4.33E-02 |  | 6.50E-03 | gm/Id plot
Using a reference current of |  |  |  |  | 5.00E-04 | 
The W/W ratio for the current mirror should be |  |  |  |  | 13.00 | 
Make assumptions about M2&3 |  |  |  |  |  | 
M2 &M3 | Vth | Vov | gm |  | Id | Lager W => easier to switch, if u can drive it
 | 0.4 | 0.2 | 0.03 |  | 3.25E-03 | 
From Razavi, The max DC voltage drop across each load resistor is (6.64) |  |  |  |  |  | 
Vr_max |  |  |  | 0.55857864 | 0.55857864 | 
Rd_max |  |  |  | 171.87 | 171.87 | 
The maximum voltage Conversion Gain can now be calculated |  |  |  |  |  | 
Av_max |  |  |  |  | 4.74 | 
Av_max (dB) |  |  |  |  | 13.5180637 | 
Note the assumptions I made here, that the common mode voltage of the LO is 0.6, with Vth of M1&M2 = 0.4 |  |  |  |  |  | 
Also I need to achieve 65mS of transconductance from M1 |  |  |  |  |  | 
The conversion gain will be reduced because of the sinusoidal input according to (6.72) |  |  |  |  |  | 
The gain reduction is a function of the diff pair equilibrium overdrive voltage and peak voltage of LO |  |  |  |  |  | 
LO_peak |  |  |  |  | 0.3 | 
Av_max_adj |  |  |  |  | 4.5401331 | 
Av_max_adj(dB) |  |  |  |  | 13.1413717 | 
To meet the gain spec (dB) |  |  |  |  | 10 | dB
Gain spec (V/V) |  |  |  |  | 3.16227766 | V/V
If R is |  |  |  |  | 200 | Ω
gm has to be at least |  |  |  |  | 2.48E-02 | S
To get this gm at an Id of |  |  |  |  | 4.00E-03 | A
Vov should be |  |  |  |  | 0.322 | V
UnCox is |  |  |  |  | 0.002 | 
The corresponding W/L ratio is |  |  |  |  | 3.86E+01 | 
at a length of |  |  |  |  | 0.06 | um
The width should be |  |  |  |  | 2.31 | um
Analysis must be modified for double-balanced topology

## Slide 11: Future work
Continue to build intuition by reading through the textbook, papers, and lecture notes
Model in excel and verify in simulation
Simulations proceeding with ideal voltage sources for biasing mixer
  Biasing will eventually be done with current mirrors
Buffer is initially ignored
  I will try to use an ideal LO by adjusting the ideal source as needed
  Buffer will later be used to create the ‘ideal’ LO